## Slide 1: The Luxury of a Hot Shower July 18-22, 2022 Petroleum Science & Technology Institute
Dr. Jon E. Olson
Professor, Hildebrand Department of
Petroleum & Geosystems Engineering

## Slide 2
Another approach for perspective on energy and power

## Slide 3
How do we use our energy?
take a hot shower?
dry your hair?
from the movie Transformers
Energy on Demand = Luxurious Living
Exercise #1

## Slide 4: A Longhorn’s Hot Shower: 1st step = collect all the data
Austin tap water temperature, 60F
hot water, 110F
shower head rate, 5 gallons/minute
average college student’s shower time
  20 minutes (?!)
how much energy to keep a Longhorn clean??

## Slide 5
Solve for
energy (in BTU’s)
to heat water
for 20 minute shower

## Slide 6: Relevant Given Information
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal
“Physics”
1 BTU heats 1 lb water by 1F

## Slide 7: Next: Approach to solve energy needed to heat water for shower
final answer, units?
BTU (energy)
amount of water, units?
lbs (mass)
change in temperature, units?
°F
“Physics”

## Slide 8: Next: Approach to solve energy needed to heat water for shower
final answer, units?
BTU (energy)
amount of water, units?
lbs (mass)
change in temperature, units?
°F
“physics” 
BTU
lbs
°F
=

## Slide 9: Next: Approach to solve energy needed to heat water for shower
amount of water in lbs?
change in temp in degF?
BTU’s needed…
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 10: Next: Approach to solve energy needed to heat water for shower
amount of water in lbs?
given Qw, ∆t, and w
find volume, Vw=
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 11: Next: Approach to solve energy needed to heat water for shower
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal
amount of water?
given Qw, ∆t, and w (rate, time and density)

## Slide 12: Next: Approach to solve energy needed to heat water for shower
amount of water?
given Qw, ∆t, and w (rate, time and density)
find volume, Vw= 5 gal/min x 20 min=100 gal
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 13: Next: Approach to solve energy needed to heat water for shower
amount of water?
given Qw, ∆t, and w
find volume, Vw= 100 gal
mass, mw = ?
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 14: Next: Approach to solve energy needed to heat water for shower
amount of water?
given Qw, ∆t, and w
find volume, Vw= 100 gal
mass, mw = volume x density = Vw x w
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 15: Next: Approach to solve energy needed to heat water for shower
amount of water?
given Qw, ∆t, and w
find volume, Vw= 100 gal
mass, mw = 100 gal x 8 lbm/gal = 800 lbm
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 16: Next: Approach to solve energy needed to heat water for shower
change in temperature?
∆T = Tfinal – Tinit = 110F – 60F = 50F

## Slide 17: Final Calculation
in words = how many BTU’s to heat 800 lbs of water by 50F
40,000 BTU
for a hot shower
Data
Tinit=60F
Tfinal=110F
Qw=5 gal/min
∆t=20 min
w=8 lbm/gal

## Slide 18: Final Calculation
40,000 BTU
for a hot shower
is that a lot of energy?
let’s see…

## Slide 19: Experiment: Energy = Work
WORK is moving a force through a distance
lifting a weight stores energy
how much energy can we store by lifting a 5 lb sack of potatoes by 5 ft?
5 lb

## Slide 20: Experiment: Energy = Work
5 lbm weighs 5 lbf
Work = Force x Distance
Work = (5.0 lbf) x (5.0 ft) = 25 ftlbf
SI conversion
5.0 lbm x 0.454 kg/lbm = 2.3 kg
5.0 ft x 0.3048m/ft = 1.5 m
F = ma = 2.3 kg * 9.8 m/s2 = 23 N
Work = (23 N) x (1.5 m) = 34 J
5 ft
5 lbm

## Slide 21: Experiment: Energy = Work
5 ft
5 lbm
we have stored energy when we lift the weight
how can we “release” the energy?
DROP the potatoes!

## Slide 22: Experiment: Energy = Work
we have stored energy when we lift the weight
how can we “release” the energy?
DROP the potatoes!
5 ft
5 lb
Convert to BTU’s
1 BTU = 778 ftlbf
31

## Slide 23
Exercise (literally) #2:
groups of 3
lifter, counter, timer
grab a sack of “potatoes”

## Slide 24: Rating your human-power generator
power = energy/time
units
  energy  BTU
  power  BTU/min
how many cycles can you do per minute?
POWER

## Slide 25: How long must our power plant work to supply energy for our shower?
Energy needed = 40,000 BTU’s
Power available =1 BTU/min

## Slide 26: How long must our power plant work to supply energy for our shower?

## Slide 27
Using 1 person to supply energy for our shower?
28 days
2,000 Aggies to provide energy in real time
Modern society demands that energy is delivered in real time, as we need it.
How many Aggies to deliver 40,000 BTU’s
in 20 minutes?

## Slide 28: Before we go…
estimate a human’s power as fraction/multiple of lawn mower engines
4 hp engine

## Slide 29: Human power in common units?
convert to horsepower
4 hp engine
1 BTU = 778 ft-lbf
1 hp = 550 ft-lbf/s
Unit conversions
= ? hp

## Slide 30: Human power in common units?
convert to horsepower
4 hp engine
we depend on our machines
machines require fuel/power

## Slide 31: Perspective on consumption and emissions…
Potato Power Video (4.5 min)

## Slide 32: Summary
energy equivalent to work, work = force * distance
lots of unit conversions!
  energy  BTU, ftlbf, J,
  power  hp, W
we take our lifestyle for granted, often unaware
modern society and our standard of living depend heavily on
  energy
  machines
  ingenuity of engineers & scientists